## Slide 1
Basic CPU Algorithm.
Read line
Cache access (if fail, mem access)
Bus access
Compute cycles
Notes: I’m not totally sure that Cache access is front of Bus access .
But I thought that because If we want to set up Bus state, we need cache state (hit or miss)
I think bus first would work better – have each CPU try to “drive” the bus in a cycle, then it broadcasts that state in the next cycle

## Slide 2: Output
Overall cycles
Compute cycles
# of Load/store
Idle cycles
Cache hit / miss
-----25 Oct ----
6. Size of overall Bus traffic(?)
7. # of Bus invaildation
8. # of access to private data
Present with Purple colored number

## Slide 3
Core 0
1. Overall cycle +=1;
cycle0 +=1;
If(compute)
2.Compute cycle+1
If(load/store)
4.Idle cycle +1
If(cycle0 == target cycle)
If(!core0_on) read line
If(load/store) 3.Load store +1
Core 1
cycle1 +=1;
If(cycle1 == target cycle)
If(!core1_on) read line
Core 2
cycle2 +=1;
If(cycle2 == target cycle)
If(!core2_on) read line
Core 3
cycle3 +=1;
If(cycle3 == target cycle)
If(!core3_on) read line
For( core 0 – 3)
corresponding
Cache[0-3] access
if(hit)
5.Cachehit
else
Cache miss , Access MEM
Cache access
Bus access

## Slide 4
# of load/store
Total instruction fil1 : 4,994,697
So then, using unsigned longlong is reasonable for ‘Cycles’ variables.
‘unsigned int’ can present 0 ~ 4,294,967,295
‘Unsigned long ’ can present 0 ~ 18,446,744,073,709,551,615

## Slide 5
Cycles
Total_cycles : timing, count cycles until end of instructions
Compute_cycles: count label==2(compute) cycles.
Total_instructions : total instructions, # of lines in a file
Num_ls : # of load/store inst
Cache_hit : cache hit
Cache_miss : cache miss
You can trace
Cache_miss*100(DRAM latency) + cache hit * 1 (hit takes 1 cycle) + compute_cycles = total_cycles.
Notes: Not sure if it would be 100 * cache miss or 117 * cache miss.
100 cycles due to DRAM latency + 1 cycle due to bus read request + 16 cycles due to bus bandwidth sending the cache block to the cache

## Slide 6
To do
DRAM, Cache structure (you can modify)
Read files
-read and translate from string to number
-access to cache
-access to dram
-set up cycles
-
-----------on me(LEE)
build cache policy (eviction LRU etc)
BUS design
How to handle mutex
…

## Slide 7
Read line
Convert string to hex
Output label, data

## Slide 8
CPU.execute ( label , data){
If(!cpu.on_process)
-> label, data = Read lines
(case)
Label 0 : memory access and mutex lock. and Set “on_process” until target cycle = latency (100)
Label 1 : memory access and mutex lock. And Set “on_process” until target cycle = latency (100)
Label 2 : compute cycle (hold). And set “on_process” until target cycle = input_data(data)
If(cycle == target cycle)
cpu.on_process = false;
}
CPU.PrintStats(){
Print stats.
Total cycles, # of load/store, compute cycles,
Cache hit,miss
}

## Slide 9
ThreadExecuteCPU( cpu, file)
While( until nothing to read ){
Read data;
CPU.execute ( label , data);
}

## Slide 10
Total cycles = 0;
While(Readfile_available){
Set Readfile_available = false;
Readfile_available = CPU1.Execute
Readfile_available = CPU2.Execute
Readfile_available = CPU3.Execute
Readfile_available = CPU4.Execute
Cycles ++;
}
Execute CPU
Execute CPU
Read_available? At least 1 file
yes